Copyright (C) 2012 Harold Grovesteen
See the file doc/fdl-1.3.txt for copying conditions.
# IPL Medium Preparation Processor Overview
The IPL Medium Preparation Processor accepts as input one or two s390 or s370 ELF executables as defined by the IPL ELF ABI Supplement. Additional content may be placed upon the IPL medium being created by use of a repository.
The first IPL ELF provides the primary IPL logic. Omitted program segments specific to the IPL ELF ABI are provided default content by the processor unless suppressed by command line arguments or explicitly provided. This IPL ELF executable is considered the “target”. The target is the program being loaded by the IPL function for execution.
The second IPL ELF is used solely as an external source for a bootstrap loader segment. A bootstrap loader is required if the size of the program precludes loading due to physical IPL medium constraints. Sample loaders are provided for all device types. If the needs of the program or device media is not satisfied by a sample loader, the IPL ELF executable may contain one of its own. In addition to medium usage and ELF content specified by the IPL ELF ABI Supplement, this document describes additional requirements for bootstrap loaders used for interfacing the loader with the preparation process. Refer to the “Bootstrap Loader Interface” section for details.
The term “executable” in this document implies an ELF executable file conforming to the IPL ELF ABI Supplement.
# IPL ELF Executable Considerations
The executable is required to contain minimally a TEXT segment. The medium preparation processor provides, if not present:
- IPL segment based upon the executable's linkage edited entry point,
- The CCW segment based upon the --device option.
- a LOWC segment (if not suppressed by the –-nolowc argument).
Because an external loader is provided by means of the IPL ELF ABI, the ELF executable identified by the –-external command-line argument must contain a LOADER program segment. The IPL ELF identified with the –-external command-line argument and the IPL ELF identified as the path/to/target argument do not need to be the same IPL ELF executable.
## Run-time Relocation
The IPL and CCW segments are used before the IPL function completes. By definition, these segments can not participate in run-time relocation. The LOWC segment is used during run-time with predefined assigned storage locations. As such it can not be relocated. However, its content may be altered during run-time and therefore storage locations addressed from within the LOWC segment may be relocated.
The IPL program may perform run-time relocation of itself with program supplied mechanisms for adjusting pointers or by use of the ELF supplied RELA section entries. Use of RELA entries requires access to the ELF section table entries. Consequently, the entire ELF must be used as the IPL program not just the TEXT segment.
The same requirements exist for an ELF used as the program loaded by a bootstrap loader segment. As a bootstrap loader program will constitute the IPL program in this context and a bootstrap loader is never the entire ELF, it must utilize non-ELF based relocation mechanisms it it requires relocation.
## Device Independent IPL ELF Executables
An executable that provides all of its own functionality and simply requires the IPL function to load the executable is referred to as a “device independent” IPL ELF executable. Such executables:
- do not provide any optional device data in the IPL segment if present or
- do not provide an IPL segment.
If bootstrap loading is required, an external loader must be specified with the --external option of the iplmed.py utility that supports the device identified by the --device option. See the “Sample Loaders” section for details of the tool kit provided loaders for each of the supported device types.
By default device independent executables will have control of the processor given to it at the entry point identified during linkage editing of the object module. This entry point is identified when the ipldpp.py utility creates the linkage editor script used for linking the executable. This location is specified by the --entry option of the ipldpp.py utility. The PSW used by the IPL function in this case will be a 64-bit S/370 EC-mode or ESA/390 PSW with the program and system mask fields set to zero and the addressing mode specified as 24-bit.
The executable can override the entry point specified during linkage editing by supplying an IPL PSW in the optional IPL segment.
Once control is passed to the executable by the IPL function or bootstrap loader, the executable operates independently of the IPL medium and its content. The executable is perfectly free to utilize the IPL medium any way it sees fit or ignore it entirely. Device independent executables may therefore be placed on any storage medium.
## Bootstrap IPL ELF Executables
Bootstrap executables utilize a bootstrap loader, also known as a stage0 loader, for loading of the target executable. The bootstrap loader functionality is provided by a LOADER segment within an IPL ELF executable. Because these executables continue interaction with the IPL medium to complete the load process, they are device dependent. See the “Bootstrap Loader Interface” section for details on how the IPL medium preparation processor communicates with the loader for the purposes of facilitating the loader's execution of its load responsibilities.

# IPL ELF ABI Usage
The IPL ELF ABI Supplement provides a specification in terms of:
- program sections in object files,
- program segments in linked executables,
- generic IPL record content, and
- system storage usage through assigned areas.
This section describes how each element of the IPL ELF ABI maps to the medium preparation processors handling of its primary elements, the IPL records. The following abbreviations are used in the following table
- EOE – end of the executable
- EOS – end of the segment
- SOE – start of the executable
- SOS – start of the segment
32-bit ABI Usage for IPL Loading
Section	Segment	Storage Area	Storage Addresses	IPL Record
.ipl[t][.area]	IPL	ASL	0x0-0x17 or	0
.asl	LOWC	ASL	0x0 or 0x8 - 0x1FF	3 / ASL and IPLP
.iplp	LOWC	IPLP	0x200-0x3FF
.text, .data	TEXT	TXT0	0x400<=SOS - EOS	2 / TXT0 or ELF1
Target executable	all	ELF1	0x1000<= SOS - EOE
.ccw	CCW	CCW	EOS+ or EOE+	1

32-bit ABI Usage for Bootstrap Loading
Section	Segment	Storage Area	Storage Addresses	IPL Record
.ipl[t][.area]	IPL	ASL	0x0-0x17 or	0
.asl	LOWC	ASL	0x0 or 0x8 - 0x1FF	3
.iplp	LOWC	IPLP	0x200-0x3FF
.loader	LOADER	TXT0	0x400<=SOS - EOS	2
.ccw	CCW	CCW	EOS+	1
Target Executable	all	any	any	4+

64-bit ABI Usage for IPL Loading
Section	Segment	Storage Area	Storage Addresses	IPL Record
.ipl[t][.area]	IPL	ASL	0x0-0x17 or	0
.asl	LOWC	ASL	0x0 or 0x8 - 0x1FF	3 / ASL and IPLP
.iplp	LOWC	IPLP	0x200-0x3FF
.text, .data	TEXT	TXT1	0x400<=SOS - EOS	2 / TXT1, TXT2 or ELF2
	TEXT	TXT2	0x1400<=SOS - EOS
Target executable	all	ELF2	0x2000<= SOS - EOE
.ccw	CCW	CCW	EOS+ or EOE+	1

64-bit ABI Usage for Bootstrap Loading
Section	Segment	Storage Area	Storage Addresses	IPL Record
.ipl[t][.area]	IPL	ASL	0x0-0x17 or	0
.asl	LOWC	ASL	0x0 or 0x8 - 0x1FF	3 / ASL and IPLP
.iplp	LOWC	IPLP	0x200-0x3FF
.loader	LOADER	TXT1	0x400<=SOS - / EOS<=0x1FFF	2
.ccw	CCW	CCW	EOS+	1
Target Executable	all	any	any	4+

## IPL ELF ABI Reserved Area Usage
The IPL ELF ABI Supplement reserves areas of storage or device content for unspecified usages. The processor and sample bootstrap loaders make use of these areas as described here.
### Main Storage
0x200-0x23F
The sample bootstrap loaders will save the Hercules IPL parameters passed in registers at these locations.
0x240-0x243
Address of the bootstrap services parameter block. See the “Sample Loaders” section for details.
0x244-0x247
Starting FBA sector of the repository inventory list supplied by the medium preparation processor.
0x248-0x24B
Size of the repository inventory list in bytes supplied by the medium preparation processor.
0x24C-0x24F – unused
0x250-0x289
If supported by the loader, the IPL Environment Information Block (IEIB) is provided in these locations. The following table identifies the fields and usage of the IEIB.
Disp.	Size	Description
+0	1	Running architecture: / 0x08 – z/Architecture / 0x04 – ESA/390 / 0x02 – System/370 Extended Control Mode / 0x01 – System/370 Basic Control Mode
+1	1	Available architectures. Uses the same bits as byte 0
+2	1	Platform information / Bits 0-3 - Platform / 0 – Physical / 1 – Hercules / 2 – Virtual machine / Bits 4-7 – I/O Options / 0x08 – DIAGNOSE X'8' available / 0x02 – Channel Subsystem I/O available / 0x01 – Channel I/O available / Hardware is assumed unless Hercules or virtual machine are detected.
+3	1	IPL Device Type: / 0x80 – Count-Key-Data device / 0x40 – Fixed-block Architecture device / 0x01 – CDROM device
+4	4	IPL device identification ( zeros implies CDROM IPL)
+8	8	LOADPARM data (ESA/390 or z/Architecture)
+16	8	Installed main storage highest addressable byte
+24	8	CPU ID as provided by STIDP (System/370 only)
+32	8	Address of System Call Control Block SCP information (ESA/390 or z/Architecture)
+40	8	Address of SYSIB 1.1.1 Basic Configuration Information (ESA/390 or z/Architecture)
+48	8	Address of the architecture support block for loader's internal usage
+48	2	IPL CPU address

### CKD DASD Content
Cylinder 0, track 0, record 4
This record is used to contain the repository inventory list.
### FBA DASD Content
Repository information is placed in the loader reserved area of the IPLP area. This corresponds to bytes 68-75 of sector 3 on the FBA IPL DASD volume and storage addresses 0x244-0x24B within the IPLP .loader section reserved area.
Sector 3, bytes 68-71
The starting sector of the repository inventory list is placed in bytes 64-67 of sector 3.
Sector 3, bytes 72-75
The size of the repository inventory list in bytes is placed in bytes 68-71 of sector 3.

# Bootstrap Loader Interface
The IPL ELF ABI Supplement provides a mechanism for a bootstrap loader to communicate with the medium preparation processor. This section describes the content and meaning of the information communicated over this interface.
The bootstrap loader interface data contains two parts:
- information provided by the loader directing the medium preparation processor how to construct the data loaded by the loader and the capabilities provided by the loader and
- information about the medium content provided by the medium preparation processor assisting the loader in performing its load responsibilities.
The next two sections details this information.
## Loader Provided Information
The first 16-bytes of a loader program segment contains the information provided by the loader to the medium preparation processor. The following content is expected by iplmed.py. Any information provided that does not conform to these requirements is treated as an error and the medium preparation process terminates.
Refer to the IPL ELF ABI Supplement for format considerations of directed or stream blocked data.

Disp.	Length	Description
+0	2	Unsigned binary value indicating the physical device block length (includes the directed block header)
+2	1	Block format for program content in ASCII (see below)
+3	1	Block format for LOWC segment content in ASCII (see below)
+4	1	End of block indicator in ASCII: “H”=directed header, “P”=physical device
+5	1	Whether records should be padded to full block size: ASCII “Y” or “N”
+6	1	Whether medium preparation process should provide the implementation specific data in the loader interface area of the segment or not: ASCII “Y” or “N”
+7	1	Supported device type and I/O architecture flags: / 0x80 – Count-Key-Data devices / 0x40 – Extended-Count-Key-Data devices / 0x20 – Fixed-Block-Architecture devices / 0x10 – tape devices / 0x08 – unit record (card) devices / 0x04 – Channel I/O architecture / 0x02 – Subchannel I/O architecture / 0x01 – CDROM device
+8	1	Supported CPU architecture flags: / 0x80 – System/370 CPU architecture / 0x40 – ESA/390 CPU architecture / 0x20 – z/Architecture CPU architecture / Bits 3-7 are reserved and must be zero.
+9	7	Reserved, must be initialized to binary zeros (0x00)

Block Format is indicated by an ASCII value:
- “S” - use stream format blocks for content
- “D” - use directed format blocks for content
- “N” - do not generate blocks for this content if present.
Any value that does not conform to those described above are considered in error and should abort the medium preparation process. Byte 6 of the loader provided information must be set to “Y” for this information to be supplied.
## Medium Preparation Provided Information
The second 16-bytes of a loader program segment contain information provided by the medium preparation processor for use by the bootstrap loader during the load process. The information provided is dependent upon the supported IPL medium.
Regardless of the medium, the last byte of the medium preparation process provided data will contain a flag indicating the class of device that must be supported by the bootstrap loader. The same flags as used by the loader in byte 7 of its supplied information are used. This provides an opportunity for the bootstrap loader to validate that it can support the IPL device.
### CDROM Devices

Disp.	Length	Description
+0	4	Bootstrapped program's entry address
+4	10	Reserved, set to zeros (0x00)
+14	1	Required bootstrap program architecture, as an unsigned binary value: / 0x24 – System/370 / 0x31 – ESA/390 / 0x64 – z/Architecture
+15	1	Required device support – 0x01 for CDROM device

### Count-Key-Data Direct Access Storage Devices

Disp.	Length	Description
+0	2	The cylinder in which the first IPL program block resides as an unsigned binary value.
+2	2	The track in which the first IPL program block resides as an unsigned binary value.
+4	1	The record identification of the first IPL program block as an unsigned binary value
+5	1	Maximum number of records on a track with the specified block size
+6	2	Maximum cylinder number on this device
+8	2	Maximum head number on this device
+10	4	Reserved, must be set to zeros (0x00)
+14	1	Required bootstrap program architecture, as an unsigned binary value: / 0x24 – System/370 / 0x31 – ESA/390 / 0x64 – z/Architecture
+15	1	Required device support: / 0x80 for Count-Key-Data device / 0x04 or 0x02 depending upon I/O architecture

### Fixed-Block-Architecture Direct Access Storage Devices

Disp.	Length	Description
+0	4	The sector number of the first sector containing IPL program content as an unsigned binary value.
+4	10	Unused, set to binary zeros (0x00)
+14	1	Required bootstrap program architecture, as an unsigned binary value: / 0x24 – System/370 / 0x31 – ESA/390 / 0x64 – z/Architecture
+15	1	Required device support / 0x20 for Fixed-Block-Architecture device / 0x04 or 0x02 depending upon I/O architecture

### Tape Devices

Disp.	Length	Description
+0	14	Unused, set to binary zeros (0x00)
+14	1	Required bootstrap program architecture, as an unsigned binary value: / 0x24 – System/370 / 0x31 – ESA/390 / 0x64 – z/Architecture
+15	1	Required device support / 0x10 for tape device / 0x04 or 0x02 depending upon I/O architecture

### Unit Record Devices

Disp.	Length	Description
+0	14	Unused, set to binary zeros (0x00)
+14	1	Required bootstrap program architecture, as an unsigned binary value: / 0x24 – System/370 / 0x31 – ESA/390 / 0x64 – z/Architecture
+15	1	Required device support / 0x08 for unit record device / 0x04 or 0x02 depending upon I/O architecture

# Program Repository
The program repository is an extension provided by the IPL Medium Preparation Processor. The repository is available only for Direct Access Storage Devices (DASD) and CDROM devices. The repository consists of programs or other content stored on the volume with a simple repository inventory. The repository is effectively a very simple read-only file system. The inventory identifies, by name, the stored content, its size in bytes, where it resides on the storage medium and, optionally, a targeted storage load location.
The program repository consists of two components:
- a Repository Content Specification that identifies the repository content to be placed on the IPL medium and
- a Repository Inventory that communicates to a running program the available content on the IPL medium.
Information about the repository is placed on the storage medium in areas reserved for the medium preparation process by the IPL ELF ABI Supplement:
- (E)CKD DASD – Cylinder 0, Head 0, Record 4 has key content in EBCDIC of “REPO” and data content consisting of the repository inventory.
- FBA DASD – Bytes 256-259 of sector 2 contains the sector number of the first sector of the repository inventory and bytes 260-263 contain the length of the inventory in bytes. Bytes 256-511 are reserved for the preparation processors usage.
- CDROM – The repository inventory is placed in the directory using the file name “REPO”. Access to the repository inventory and repository content requires use of service processor input/output functions provided as part of the SERVC instruction.
The program repository is considered a part of the application loaded during the IPL function. Support for accessing the repository may be provided by the either the bootstrap loader via the services parameter block or directly by the IPL ELF executable.
The program repository may also reside directly in the Hercules host file system if the Host Resource Access Facility is available and enabled. In this case the Repository Content Specification may be used directly or processed into an inventory for use. The IPL parameters supplied in registers 0 through 15 may used to locate the content specification or inventory in the host file system.
## Repository Content Specification
The repository content is specified by means of a host text file identified by the –-repo command line option. A host file destined for the repository is identified by a single line in the file with the following parameter syntax:
name host_file_path [target_load | *] [BRANCH | CALL | LOAD]
The meaning of the parameters are as follows:
- name - A one to eight character name identifying the content in the repository. The name must start with an alphabetic character and be followed by optional alphanumeric characters.
- host_file_path – The host path to the file whose contents will be placed on the repository. The content must have a length greater than zero. Environment variables encountered in the host_file_path parameter are expanded by the processor.
- target_load – The optional address at which the content should be placed in storage. The default, *, loads the file at the start of the next 4K page boundary. The target_load is initialized to 0x10000. No requirement exists for the content to actually be loaded at the target location. Executable relocation must be accommodated if an executable is loaded anywhere other than its linkage editor load address. '*' is only adjusted for content flagged for loading. How the current location is adjusted is implementation specific.
- BRANCH – Indicates that this content is to be loaded and entered via a branch to the ELF entry point. “LOAD” is implied.
- CALL – Indicates that this content is to be loaded and entered via a call to the entry point using the main process entry function signature. “LOAD” is implied.
- LOAD – Indicates this content should be loaded but not entered.
Comments start with a “#” character at any point on the line. A statement lacking any parameters is ignored.
## Repository Inventory
The repository inventory entry has the following format. The general structure is the same for each storage medium. Some fields are device specific. Content name is constrained to eight characters by the CDROM SERVC real interface limitation. “Type” indicates whether the field is required (“R”) in a repository inventory or available for implementation (“I”) use.
Disp.	Length	Type	Format	Description
+0	8	R	character	EBCDIC name of the content, left justified and space filled with 0x40.
+8	8	R	unsigned binary	Targeted load address.
+16	4	R	unsigned binary	Size of this repository content in bytes
+20	4	I	Device specific	Starting location of this content: / (E)CKD – two unsigned two-byte binary values indicating the starting cylinder and head of the content, respectively (CCHH) / FBA – sector number of the first sector of the content / CDROM – not used, zero
+24	2	I	unsigned binary	Size in bytes of the logical stream record. Not used by CDROM
+26	1	I	unsigned binary	Number of device units with regards to the logical record: / (E)CKD – number of logical records per track / FBA – number of sectors per logical record / CDROM – not used, zero
+27	1	I	unsigned binary	(E)CKD only – number of tracks per cylinder
+28	3	I	available	Must be binary zeros if not used
+31	1	R	Flag bits	Flag bits: / 0 – ENTER this content / 1 – Entry method (0 is branch, 1 is a function call) / 2 – LOAD specified content / 3 – target load address is current location / 4,5 – reserved, should be zeros / 6 – set to one, indicates an implementation specific entry / 7 – set to one, indicates the last entry

The eleven bytes at displacements 20 through 30 are available for implementation specific use. The above descriptions are for use with a IPL medium that supports a repository.
By setting bit 6 of byte 31 of an entry to one, the repository entry may be reserved for use by the program. Any number of entries are allowed for this purpose. Byte 31 remains reserved but the implementation may use for any purpose bytes 0-30 of the entry for its use. See the next section, “Boot Parameters”, for a description of the default use of implementation specific entries.
### Boot Parameters
The default usage of implementation specific repository entries is to provide boot parameters to the bootstrap loader. What the bootstrap or other program does with this information is undefined.
The boot parameter specification statement is as follows:
$boot parm1 [ parm2 ... ]
or
$boots “string”
In the case of the $boot specification, excess spaces are removed and the result is placed in bytes 0-30 of the implementation specific repository entry.
In the case of the $boots specification, the contents of the string are placed in the entry terminated by a 0x00 byte.
In both cases the ASCII characters are converted to EBCDIC.

# Sample Loaders
The sample loaders are provided:
- as examples of how to utilize the facilities provided by the IPL Medium Preparation Processor,
- tests of the processor's functionality and
- reusable loader functionality provided by the toolkit.
In other words, the goal of the sample loaders is that they may be used directly without additional development.
The sample loaders are provided in the ./test/bin/ipl directory, relative to the SATK install directory. The following files provide embedded loaders usable by the --external option of the iplmed.py utility.
- cardmbed – Card device bootstrap loader
- cdrommbed – CDROM device bootstrap loader
- ckdmbed – CKD device bootstrap loader
- fbambed – FBA device bootstrap loader
- tapembed – Tape device bootstrap loader
Each of the sample IPL ELF loaders is embedded with a sample device independent “hello world” IPL ELF executable. The source for this is located at test/src/ipl/default.S.
## Bootstrap Services Parameter Block (BSPB)
The Bootstrap Services Parameter block provides run-time linkage between the loaded IPL ELF or repository content and the bootstrap loader. The format and use of the BSPB, as well as its location, are implementation specific. However, the fixed location in real storage at 0x240-0x243 allows the running program to locate the parameter block. The mechanism by which a service is called is also implementation specific. An example of how this can be utilized is provided by the hstage0 implementation. The following section provides details of the hstage0 implementation.
## hstage0 – a Host Resource Access Facility Bootstrap Loader
hstate0 is a stand-alone external bootstrap loader. In the context of this document, hstage0 is an IPL ELF executable in its own right. In this regard it is unlike the other bootstrap loaders, the intent of which are for use in conjunction with an IPL ELF that is itself the target of the bootstrap process.

# iplmed.py Command Line Options
iplmed.py is the utility that creates an instance of IPL media for use with the Hercules emulator. It takes as input an IPL ELF and based upon the options transforms it into a Hercules emulated medium that may participate in the IPL function.
The basic command line for the IPL medium preparation processor, iplmed.py is as follows:

iplmen.py --medium=xxx [options] path/to/target

The path to the target IPL ELF executable is required.
Options that describe the IPL medium:
--medium=	Provides the path and file name of the Hercules emulated device that will contain the IPL program. This option is required.
--device=	Targeted device type and model. If a loader does not support this device as specified in the loader information data, an error condition is detected and the IPL medium is not created.
--trunc	The minimal size emulated file will be used for storing the IPL records.
--compressable	The minimal size emulated file will be used allowing for use of compression. A separate Hercules utility must be used to actually compress the emulated medium.
Options that control the IPL bootstrap process.
--external=	Forces the IPL process to load the identified external loader which will then load the IPL ELF executable. If specified, --external identified an IPL ELF executable that contains a LOADER segment. This bootstrap loader is extracted from the IPL ELF executable and used with or instead of a LOADER segment present in the target IPL ELF executable. This option allows an embedded loader to be reused in other targets.
--nolodr	Suppresses use of any embedded or external loader. If used, --nolodr overrides --external.
--bootelf	Forces a loader to load the entire IPL ELF executable regardless of the IPL ELF text segment flag. The text segment flag is determined by whether the original ELF object file contained an IPL section starting with “.iplt” (boot TEXT segment only) or “.ipl” (boot entire IPL ELF). This option overrides “.iplt” in the object file when a loader is used.
--nolowc	If a LOWC segment is present in the IPL ELF executable it will be suppressed and not placed on the IPL medium.
--noboot	Suppresses writing of boot program CARD records. Ignored by all other media types.
Options that check a loader's capabilities:
--arch=	Validates that the loader supports this architecture. Acceptable values are: 24 (S/370), 31 (ESA/390) or 64 (z/Architecture). If the loader does not support the specified architecture as defined in its loader interface data, an error is detected and the medium is not created.
--ioarch=	Validates that the loader (either supplied externally or embedded wthin the IPL ELF) supports this I/O architecture. Acceptable values are: chan (S/370 channel-based I/O architecture) or sch (subchannel-base I/O architecture). If the loader does not support the specified architecture as defined in its loader interface data, an error is detected and the medium is not created.
Options that effect the utility's output:
--debug	Provide additional information during IPL medium generation to assist in problem resolution.
--s370bc	Create a S/370 basic control mode IPL PSW rather than a S/370 extended control mode PSW (or its identical ESA/390 PSW). A IPL PSW is provided only when one is not present in the IPL ELF.

# ipldpp.py Command Line Options
Creation of the IPL ELF executable requires assistance on the part of the linkage editor. The ipldpp.py utility pre-processes an elf object module and generates a linkage editor script that will transform the object file into an IPL ELF conforming executable. This utility provides ld pre-processing, hence the name ipldpp.py. The utility understands the various special sections, storage areas and their usage as defined by the IPL ELF Supplement.
The ipldpp.py utility uses the following command line format:

ipldpp.py --lds=xxx [options] path/to/elf_object_file

The path to the ELF object file is required.
All options affect the utility output, as follows:
--lds=	The generated linker script path and file name. This option is required.
--entry=	The entry point as identified in the IPL ELF executable. This is not necessarily the IPL PSW instruction address, but can be. The value specified must be a global externally referenced symbol name.
--load=	A hexadecimal value identifying where in storage the IPL ELF executable will be loaded.
--relo	If this option is provided, the IPL ELF executable will contain the linkage editor supplied relocation information. This is required if the IPL ELF will use this information for relocation purposes. Otherwise, this information will not be present in the executable.
--debug	If present provides additional information for problem resolution purposes.